## Slide 1: SPH simulation of vertical high-speed jet flow from a circular nozzle with stagnation pressures prediction
MOREIRA*, P. Manso**, D. VIOLEAU*** AND F. TAVEIRA-PINTO*
*University of Porto – Faculty of Engineering, Porto, Portugal
** Ecole Polytechnique Fédérale de Lausanne (EPFL), Lausanne, Switzerlan
***EDF R&D / LNHE & Université Paris-Est, Saint-Venant Hydraulics Laboratory (ENPC, EDF R&D, CEREMA), Chatou, France
SPHERIC 2019
Exeter, England – 25th – 27th June

## Slide 2: CONTENTS
MOTIVATION
STUDY GOALS
EXPERIMENTAL BACKGROUND
3D NUMERICAL MODEL
RESOLUTION SENSITIVITY ANALYSIS
RESULTS
CONCLUSION

## Slide 3: MOTIVATION
MOTIVATION
1
STUDY GOALS
EXPERIMENTAL…
3D NUM..
GPUSPH FORMULATIONS
RESULTS
2
3
4
5
6
CONCLUSION
7
Why this topic?
Caniçada dam, Portugal
High-velocity plunging jets can be found in many dams
There is a need to quantify the HYDRODYNAMIC LOADING produced by the jet impact
Unrevised probable maximum floods
+
Climate change
=
Increased risk of dam overtopping

## Slide 4: STUDY GOALS
To understand the physics of the diffusion of jets in pools for various pool depths, as such analysis is hampered in a physical model due to the high ratio of entrained air;
To provide quantification of the pressures acting on the pool bottom;
To contribute to the continuous verification and validation of the SPH method.
MOTIVATION
1
STUDY GOALS
EXPERIMENTAL…
3D NUM..
GPUSPH FORMULATIONS
RESULTS
2
3
4
5
6
CONCLUSION
7

## Slide 5: EXPERIMENTAL BACKGROUND
MOTIVATION
1
STUDY GOALS
EXPERIMENTAL…
3D NUM..
GPUSPH FORMULATIONS
RESULTS
2
3
4
5
6
CONCLUSION
7
Pressures were measured at the bottom of the pool
Experiments previously done at EPFL
Manso (2006) studied jets with an exit velocity of ~29.5 m/s (Q=120 L/s) impinging into a still water pool of varying water depths, Y

## Slide 6: 3D NUMERICAL MODEL
(same dimensions as the physical model)
Tube diameter, D: 0.072 m (not modelled)
Pool diameter: 3 m
Pool water depth, Y: 0.2 m
MOTIVATION
1
STUDY GOALS
EXPERIMENTAL…
3D NUM..
GPUSPH FORMULATIONS
RESULTS
2
3
4
5
6
CONCLUSION
7
Formulations used in GPUSPH 4.1:
USAW – boundary conditions (Ferrand et al. 2012)
Open-boundaries (Ferrand et al., 2017); a velocity driven (inlet) and two pressure driven (outlets, to mimic the weirs existent in the physical model)
Standard k-ε turbulence model
Time-step varied (maximum CFL number of 0.3 – stability condition)
Quintic Wendland kernel

## Slide 7: 3D NUMERICAL MODEL
On June 13th 2019!
MOTIVATION
1
STUDY GOALS
EXPERIMENTAL…
3D NUM..
GPUSPH FORMULATIONS
RESULTS
2
3
4
5
6
CONCLUSION
7
New features:
possibility to create simulation scenarios using the SALOME open-source platform;
Hu & Adams formulation for multi-fluid;
additional models for the viscous contribution to Navier–Stokes (Monaghan, Español & Revenga);
more sophisticated viscous model options, including turbulence, averaging operator and fluid rheology;
non-Newtonian rheology models including Bingham, granular material, Herschel–Bulkley and DeKee & Turcotte;
man-machine interface;
experimental support for initial repacking phase.
The GPUSPH Discourse group is now available
visit www.gpusph.org & www.gpusph.discourse.group

## Slide 8: RESOLUTION SENSITIVITY ANALISYS
MOTIVATION
1
STUDY GOALS
EXPERIMENTAL…
3D NUM..
RESOLUTION SENSITIVITY..
RESULTS
2
3
4
5
6
CONCLUSION
7
D/dp = 7,1
D/dp = 17,2
D/dp = 34,1
Chart: D/dp
| 7.1 | 17.2 | 23.9 | 34.1
U relative error | 22.0339 | 18.6441 | 12.5424 | 9.1525
No. Of parts. | 1.7 | 19 | 52 | 150
Using a variable resolution approach would be ideal (higher resolution in the noozle and lower resolution in the pool), but this is not yet available in GPUSPH.
D/dp = nozzle diameter/ particle diameter
Initial simulations showed that the flow inside the nozzle was too much accelerated (!?)
Thus the exit velocity wasn’t accurate…

## Slide 9: RESOLUTION SENSITIVITY ANALISYS
MOTIVATION
1
STUDY GOALS
EXPERIMENTAL…
3D NUM..
GPUSPH FORMULATIONS
RESULTS
2
3
4
5
6
CONCLUSION
7
The adopted solution was to impose a logaritmic profile at the nozzle’s exit and to not simulate the nozzle itself
Chart: U/Umax
| 0 | 0.55747413999999995 | 0.71496605999999996 | 0.86244069999999995 | 0.94993620000000001 | 0.99475539999999996 | 0.99454109999999996 | 0.99182694999999998 | 0.99161270000000001 | 0.98127390000000003 | 0.98605936999999999 | 0.96588180000000001 | 0.96309626000000004 | 0.96291769999999999 | 0.96277489999999999 | 0.99755879999999997 | 0.99736239999999998 | 0.96966739999999996 | 0.83467424000000001 | 0.65718330000000003 | 0
Manso et al. (2008); with grid and vent; U=30.5 m/s | 0.0063842 | 0.0090629 | 0.011876 | 0.02076 | 0.022322 | 0.085629 | 0.16063 | 0.23559 | 0.31059 | 0.42917 | 0.50426 | 0.56641 | 0.66637 | 0.72887 | 0.77887 | 0.8545 | 0.92326 | 0.99152 | 0.98911 | 0.98594 | 0.98759
Manso et al. (2008); without grid and vent; U=29.5 m/s | 0 | 0.02134 | 0.053172 | 0.072325 | 0.15407 | 0.22943 | 0.36019 | 0.44761 | 0.56016 | 0.67887 | 0.75392 | 0.84173 | 0.91656 | 0.95339 | 0.97737 | 0.99388
SPH with nozzle; U~32.2 m/s; D/dp=34.1 | 0 | 0.024845 | 0.049689 | 0.13043 | 0.20497 | 0.26501 | 0.32712 | 0.40787 | 0.49068 | 0.5735 | 0.67288 | 0.7619 | 0.85714 | 0.91718 | 0.96066 | 0.98344 | 0.99586
Velocity profile along the nozzle diameter at the exit section
In terms of the velocity profile shape, modeling the nozzle is indeed more accurate, but it demands for an impractically high number of particles

## Slide 10: RESULTS
Photo from Lopes (2005)
MOTIVATION
1
STUDY GOALS
EXPERIMENTAL…
3D NUM..
GPUSPH FORMULATIONS
RESULTS
2
3
4
5
6
CONCLUSION
7
Qualitative validation
10-s simulation
Notes: We made considerations on the impact of analysing only 10s of simulations in our paper 3 (under review in JHR)

## Slide 11: RESULTS
Photo from Lopes (2005)
MOTIVATION
1
STUDY GOALS
EXPERIMENTAL…
3D NUM..
GPUSPH FORMULATIONS
RESULTS
2
3
4
5
6
CONCLUSION
7
Quantitative validation
Chart: Y/D
| 2.7777777777777781 | 2.7777777777777781 | 5.5555555555555562 | 5.5555555555555562 | 8.3333333333333339 | 8.3333333333333339 | 2.7777777777777781 | 5.5555555555555562 | 8.3333333333333339
SPH | 4.12 | 8.1 | 3.67 | 8.65 | 2.89 | 7.3 | 1.36 | 0.94 | 0.5
Manso (2006) | 5.28 | 8.01 | 5.3 | 8.25 | 4.8 | 8.05 | 1.1 | 0.64 | 0.33
Free-surface particles in red detected following a simplification of the technique proposed by Marrone, Colagrossi, Le Touzé & Graziani, (2010)
Pressure at the stagnation point for Y/D= 2.8; Y/D= 5.6; Y/D= 8.3
Results on the SPHERIC’s paper - Y/D= 2.8
Y/D= 2.8
Y/D= 5.6
Y/D= 8.3
Consistent with the air entrainment visible in the experiments

## Slide 12: RESULTS
6 SPH simulations(2005)
MOTIVATION
1
STUDY GOALS
EXPERIMENTAL…
3D NUM..
GPUSPH FORMULATIONS
RESULTS
2
3
4
5
6
CONCLUSION
7
Quantitative validation
Pressure at the stagnation point (Y/D= 2.8; Y/D= 4.2; Y/D= 5.6; Y/D= 7.2 Y/D= 8.3; Y/D= 9.7)
Chart: Y/Dj
| 0 | 2 | 4 | 4.5 | 4.5 | 5 | 5.4 | 6 | 6.19 | 6.19 | 6.5 | 7 | 7.5 | 8 | 8.5 | 9 | 9.5 | 10 | 10.5 | 11 | 11.5 | 12
Best fit Ervine at al. (1997) | 0.86 | 0.86 | 0.86 | 0.86 | 0.86 | 0.86 | 0.86 | 0.69333 | 0.65142 | 0.65142 | 0.59077 | 0.50939 | 0.44373 | 0.39 | 0.34547 | 0.30815 | 0.27657 | 0.2496 | 0.22639 | 0.20628 | 0.18873 | 0.17333
SPH | 0.85817 | 0.8499 | 0.78047 | 0.72764 | 0.60779 | 0.46922
Manso (2006) 17.5<U<27 m/s | 0.78676 | 0.72994 | 0.53546 | 0.40211 | 0.82353 | 0.80203 | 0.57594 | 0.3909 | 0.86997 | 0.8517 | 0.68241 | 0.45373 | 0.87165 | 0.86791 | 0.73183 | 0.47469 | 0.97834 | 0.96807 | 0.84031 | 0.43841
Bollaert (2002) results envelope | 0.93665 | 0.9276 | 0.93665 | 0.95475 | 0.8009 | 0.70136 | 0.63801 | 0.61538 | 0.44796 | 0.45701 | 0.42986 | 0.38462 | 0.33937 | 0.23982 | 0.095023 | 0.12217 | 0.15837 | 0.23529 | 0.24887 | 0.26697 | 0.42081 | 0.54299 | 0.52036 | 0.61538 | 0.61086 | 0.65158 | 0.65611 | 0.63801 | 0.68326 | 0.71946 | 0.77828 | 0.90045 | 0.93665
Manso (2006) U=29.5 m/s | 0.97101 | 0.98481 | 0.85713 | 0.4405

## Slide 13: CONCLUSIONS
A very fine particle resolution is needed to accurately simulate the confined flow
Qualitative results are sound
Mean and maximum pressures near the stagnation point were computed with a relative error of about 22% and 1% (Y/D= 2.8)
Accuracy of the mean pressure’s prediction was likely influenced by the lack of air phase modelling
Further analysis will include:
- centerline velocity decay along the jet
- radial pressures’ distribution
MOTIVATION
1
STUDY GOALS
EXPERIMENTAL…
3D NUM..
GPUSPH FORMULATIONS
RESULTS
2
3
4
5
6
CONCLUSION
7

## Slide 14: THANK YOU!
QUESTIONS AND COMMENTS CAN BE SEND TO: up200706631@fe.up.pt